## Slide 1
From Sample Preparation to Sequencing:
Experimental Design, Library Preparation
and Sequencing: 10x and SMART-Seq
Annelien Verfaillie
25th Feb 2021

## Slide 2
Notes: You have a biological question and you are looking for the best way to answer. We are here today to give you an insight in how RNA-seq works and how it might fit into your scientific work and help you get some of your answers to your questions.
Just like any experiment RNA-seq starts with a good experimental design. Once you have this in place you can move into preparing and executing the experiments to gather your data. You then proceed to analysing this data to look at what answers you can find with regards to your question.

## Slide 4
What is my scientific question?
Notes: There are many single cell techniques being developed, some more experimental than others.

## Slide 5
retaining spatial information
What is my scientific question?
10x visium
yes
no
interested in DNA or RNA
Notes: Implication on input material, cost and time of your experiment.

## Slide 6
retaining spatial information
What is my scientific question?
10x visium
yes
no
interested in DNA or RNA
Interested in epigenetics
DNA
Notes: Implication on input material, cost and time of your experiment.

## Slide 7
retaining spatial information
What is my scientific question?
10x visium
yes
no
interested in DNA or RNA
Interested in epigenetics
yes
10x ATAC
scBS seq
Cut and run
Methylation
…
no
scDNA seq
DNA
Notes: Implication on input material, cost and time of your experiment.

## Slide 8
retaining spatial information
What is my scientific question?
10x visium
yes
no
interested in DNA or RNA
Interested in epigenetics
yes
10x ATAC
scBS seq
Cut and run
Methylation
…
no
scDNA seq
DNA
3’ vs 5’ mRNA
RNA
Notes: Implication on input material, cost and time of your experiment.

## Slide 9
retaining spatial information
What is my scientific question?
10x visium
yes
no
interested in DNA or RNA
Interested in epigenetics
yes
10x ATAC
scBS seq
Cut and run
Methylation
…
no
scDNA seq
DNA
3’ vs 5’ mRNA
10x 5’ immune profiling
Full
transcript?
3’
5’
RNA
Notes: Implication on input material, cost and time of your experiment.

## Slide 10
retaining spatial information
What is my scientific question?
10x visium
yes
no
interested in DNA or RNA
Interested in epigenetics
yes
10x ATAC
scBS seq
Cut and run
Methylation
…
no
scDNA seq
DNA
3’ vs 5’ mRNA
10x 5’ immune profiling
Full
transcript?
3’
5’
SMART-seq
10x RNA seq
yes
no
RNA
Notes: Implication on input material, cost and time of your experiment.

## Slide 11
retaining spatial information
What is my scientific question?
10x visium
yes
no
interested in DNA or RNA
Interested in epigenetics
yes
10x ATAC
scBS seq
Cut and run
Methylation
…
no
scDNA seq
DNA
3’ vs 5’ RNA
10x 5’ immune profiling
Full
transcript?
3’
5’
SMRT-seq
10x RNA seq
yes
no
RNA
Notes: Implication on input material, cost and time of your experiment.

## Slide 12
SMART-seq vs 10x 3’ RNA seq
 | SMART seq | 10x 3’ RNA
RNA type | mRNA* | mRNA
transcript | full | 3’ end
sensitivity | high | medium
sequencing | deep | shallow
Cost per cell | high | medium
Single cell “seperation” | 96-well plate | droplet formation
throughput | Low | high
Detecting heterogeneity | low | high
Specific properties | Focus on subpopulations via FACS sorting | Feature barcoding
* There is now an experimental protocol aiming for total RNA
Notes: Implication on input material, cost and time of your experiment.

## Slide 13
My scientific question is “and” and not “or”
Multi-omics in single cell sequencing
+ATAC
M&T seq
NMT seq
transcrip tome
genome
epigenome
proteome
G&T seq
CITE-seq
Notes: single-cell nucleosome, methylation and transcription sequencing

## Slide 14
What do I need?
Starting material
  Single cell or nuclei suspension
    Cell lines > Fresh tissue > Frozen tissue
  Avoid frozen or fixed cell suspension if possible
  Consider timing and processing

## Slide 15
What do I need?
Starting material
  Single cell or nuclei suspension
    Cell lines > Fresh tissue > Frozen tissue
  Avoid frozen or fixed cell suspension if possible
  Consider timing and processing
Sufficient conditions to draw your conclusions
  drug vs no drug , cancer vs normal
  note that the experimental question is crucial
    do you want to explore (what is my tissue made up of)
    do you want to link presence/absence of clusters/cell types to your condition

## Slide 16
What do I need?
Starting material
  Single cell or nuclei suspension
    Cell lines > Fresh tissue > Frozen tissue
  Avoid frozen or fixed cell suspension if possible
  Consider timing and processing
Sufficient conditions to draw your conclusions
  drug vs no drug , cancer vs normal
  note that the experimental question is crucial
    do you want to explore (what is my tissue made up of)
    do you want to link presence/absence of clusters/cell types to your condition
What about replicates?

## Slide 17
Single cell and replicates
Technical
  Correct for variation due to sample handling
Biological
  Correct for variation in the population
https://assets.ctfassets.net/an68im79xiti/3Q2nLWJ3hu6oIQWu8u66kQ/c2f2d89c1487131abc9a60cf89d00766/CG000170_TechNote_BiologicalandTechnicalVariationinSingleCell3_GeneExpressionExperiments_RevA_.pdf
Notes: However is this what a replicate means in a single cell experiment

## Slide 18
What does “biological replicate” mean in single cell
Within one sample  cells of a similar type can be considered a replicate of each other
Biological replicates can show different clustering when driven by genetic background and not by altered gene expression
Single cell and replicates

## Slide 19
Set up experiment
generate single cell suspensions
QC
Library prep
the genomics core (or you)
You

## Slide 20
Set up experiment
generate single cell suspensions
QC
Library prep
the genomics core (or you)
You

## Slide 21
Preparing single cell suspensions
Fresh material
Frozen material
cells
nuclei
tissue specific methodology
Requires optimization
Mechanical and/or enzymatic dissociation

## Slide 22
Preparing single cell suspensions
Fresh material
Frozen material
cells
nuclei
Mechanical and/or enzymatic dissociation

## Slide 23
Preparing single cell suspensions
Fresh material
Frozen material
cells
nuclei
Mechanical and/or enzymatic dissociation
tissue specific methodology
Requires optimization

## Slide 24
Preparing single cell suspensions
Fresh material
Frozen material
cells
nuclei
Process right away
Storing cell suspension
Mechanical and/or enzymatic dissociation
DMSO based freezing
Fixation methods:
Methanol, paraformaldehyde
tissue specific methodology
Requires optimization
“unmodified”
“modified”
Cell hashing
Antibody labeling
…

## Slide 25
viability
debris
clumps
QC single cell suspensions
Sufficient cells

## Slide 26
viability
debris
clumps
QC single cell suspensions
Sufficient cells

## Slide 27
Filtering: a balance of time, removal and cleanliness
Simple filters:
  + Fast
  + Good for large debris and clumps
  doesn’t remove ambient material or small debris
  Can cause cloggs and cell loss
FACS sorting
  + Good for smaller debris and ambient material
  - Time consuming
  - Dilution of sample volume
Centrifugation gradient, specialized columns, dead cell removal kits, RBC lysis
QC single cell suspensions

## Slide 28
Preparing single cell suspensions
SMART-seq
10x
FACS sorting into 96 well plate
1 cell per well
Directly into lysis buffer
Positive controls
Negative controls
Tube with at least 50,000 cells/50 µl
PBS with low BSA content
Clump and debris free
Tagged or treated (feature barcoding)

## Slide 29
Set up experiment
generate single cell suspensions
QC
Library prep
the genomics core (or you)
You

## Slide 30
Library prep: SMART-seq

## Slide 31
Library prep: 10x 3’ RNA-seq
Cell suspension

## Slide 32
Library prep: 10x 3’ RNA-seq
Loading vs recovering
1) Volume and cell concentration

## Slide 33
Library prep: 10x 3’ RNA-seq
Loading vs recovering
1) Volume and cell concentration
2) droplet formation
Not all gems have a cell
60-70% recovery

## Slide 34
Library prep: 10x 3’ RNA-seq
Loading vs recovering
1) Volume and cell concentration
2) droplet formation
Not all gems have a cell
60-70% recovery
3) Overloading  doublets

## Slide 35
Library prep: 10x 3’ RNA-seq

## Slide 36
Library prep: 10x feature barcoding

## Slide 37
Library prep: 10x feature barcoding

## Slide 38
Library prep: cell hashing
1 channel = 1 library = ~10,000 cells

## Slide 39
Library prep: 10x ATAC seq

## Slide 40
Library prep: 10x ATAC seq

## Slide 41
Library prep: 10x ATAC + RNA seq
1 sample but 2 libraries

## Slide 42
Library prep: 10x visium

## Slide 43
Sequencing

## Slide 44
SMART seq
Single read 50 bp is sufficient
Unique cell identifier info is in the standard indexing
1-2M reads per cell is sufficient
Sequencing

## Slide 45
10x RNA seq
Unique cell identifier info is in read 1
Unique configuration: 28-8-8-91
25000 reads per cell
Feauture barcoding and cell hashing
  identical configuration
  Less reads per cell
Sequencing

## Slide 46
10x RNA seq
Unique cell identifier info is in read 1
Unique configuration: 28-8-8-91
25000 reads per cell
Feauture barcoding and cell hashing
  identical configuration
  Less reads per cell
10x ATAC seq
25000 reads per cell
unique cell identifier info is in index2
Configuration is 150-8-16-150
Sequencing

## Slide 47
10x staggered sequencing approach:
How successful is my library?
  QC of a library does not reveal all
Sequencing

## Slide 48
10x staggered sequencing approach:
How successful is my library?
  QC of a library does not reveal all
1) degraded RNA  library profile is fine but TSO primer
2) ambient RNA  library profile ok but no clear cell distinction
3) nr of cells captured
4) saturation level
Sequencing

## Slide 49
Sequencing
10x staggered sequencing approach:
Shallow seq: 3000-5000 reads per cell (~20% of recommended)
1) good estimate of true captured cells
2) Indication of required depth (ie saturation level)
  We can combine several projects on a shallow run to make it more price efficient.

## Slide 50
Sequencing
10x staggered sequencing approach:
Shallow seq: 3000-5000 reads per cell (~20% of recommended)
1) good estimate of true captured cells
2) Indication of required depth (ie saturation level)
B. Deep sequencing:
  based on the above results  re-estimate the true required reads needed
  samples that do not generate reliable data can be eliminated

## Slide 51
Interesting literature
Sample prep, replicates and experimental set up
https://www.nature.com/articles/s41591-020-0844-1/#Sec1
https://www.nature.com/articles/s12276-018-0071-8
https://genomemedicine.biomedcentral.com/articles/10.1186/s13073-017-0467-4
https://www.onlinelibrary.wiley.com/doi/full/10.1002/cyto.a.23690
https://assets.ctfassets.net/an68im79xiti/3Q2nLWJ3hu6oIQWu8u66kQ/c2f2d89c1487131abc9a60cf89d00766/CG000170_TechNote_BiologicalandTechnicalVariationinSingleCell3_GeneExpressionExperiments_RevA_.pdf
https://www.10xgenomics.com/resources/support-documentation/
https://www.nature.com/articles/s41591-018-0096-5
Overview of interesting single cell techniques
https://science.sciencemag.org/content/358/6359/69.full
https://www.whatisepigenetics.com/overview-single-cell-epigenomics-methods/
https://www.nature.com/news/single-cell-sequencing-made-simple-1.22233

## Slide 52
You are all set to start your first single cell sequencing experiment!
Still not sure on how to proceed?
Contact the Genomics Core for more info
info@genomicscore.be